## Slide 1
SOLAR-POWERED IoT WATER MONITORING
AquaTracker
Real-time pH, turbidity and water-level tracking with automatic SMS alerts — built on Arduino UNO and GSM, running entirely off-grid on solar power.
Interview Project Showcase

## Slide 2
Problem Statement
Why manual water monitoring falls short
No visibility
Overhead and underground tanks are checked physically — problems are found only after they happen.
Unsafe water goes unnoticed
pH imbalance and rising turbidity are invisible to the eye until water is already unsafe to use.
Overflow & wastage
Tanks overflow silently, wasting pumped water and electricity, especially in unattended installations.
No remote power option
Traditional monitoring setups need mains power and Wi-Fi, ruling out farms, rooftops and remote sites.
AquaTracker
2

## Slide 3
Where AquaTracker Fits
Practical use cases across everyday water systems
Homes & apartments
Rooftop / sump tank overflow prevention and drinking water quality checks.
Agriculture
Irrigation tanks and farm ponds monitored for level and turbidity, off-grid on solar.
Industrial sites
Process water and effluent tanks tracked continuously without manual rounds.
Remote / rural areas
No mains power or broadband needed — solar + GSM covers areas Wi-Fi can't.
AquaTracker
3

## Slide 4
Why AquaTracker Is Convenient
Designed to run itself, on-site, with zero manual checks
Fully solar powered
12V battery charged by a solar panel — works continuously with no mains electricity dependency.
Alerts come to you
No app or dashboard to check — SMS alerts land directly on any basic mobile phone via GSM.
Call-and-check
Anyone can call the device's SIM number and instantly get an SMS back with live readings.
Low-cost, simple hardware
Built entirely on an Arduino UNO with off-the-shelf sensors — easy to replicate and maintain.
AquaTracker
4

## Slide 5
Aligned with the UN Sustainable Development Goals
AquaTracker directly supports SDG 6: Clean Water and Sanitation
GOAL 6
Clean Water
and Sanitation
United Nations
Sustainable Development Goal
Safe drinking water monitoring
Continuous pH and turbidity tracking helps catch unsafe or contaminated water early, supporting SDG target 6.1 on safe and affordable drinking water.
Reducing water wastage
Overflow alerts prevent silent tank overflow, cutting down on wasted treated water in line with SDG target 6.4 on water-use efficiency.
Sustainable, off-grid operation
Solar power keeps monitoring running without adding to grid electricity demand, keeping the solution itself low-impact.
Extending access to underserved areas
Low-cost, GSM-based alerts bring quality monitoring to rural and remote communities that lack smart water infrastructure.
AquaTracker
5

## Slide 6
System Architecture
Solar-charged battery → Arduino UNO → sensors → GSM → SMS to user
AquaTracker
6

## Slide 7
Hardware Components
Every block in the architecture, and the job it does
Component | Role in the system
Solar panel + 12V battery | Off-grid power source; keeps the unit running continuously without mains electricity
Arduino UNO | Central controller — reads all sensors, runs the logic, drives the display and GSM module
pH sensor (analog) | Measures acidity/alkalinity of the water sample
Turbidity sensor (analog) | Measures water clarity / suspended particles
HC-SR04 ultrasonic sensor | Measures distance to the water surface to calculate tank level
SIM800/900 GSM module | Sends SMS alerts and replies to incoming calls with live readings
SSD1306 OLED display | Shows live pH, level and quality readings on-site
AquaTracker
7

## Slide 8
How It Works
The read → evaluate → alert cycle, repeated continuously
1
Power up
Solar panel keeps the 12V battery topped up; Arduino & GSM run off it directly.
2
Read sensors
pH, turbidity and ultrasonic level are sampled and noise-filtered every cycle.
3
Compute readings
Calibrated formulas turn raw voltages into real pH, NTU, °C and level %.
4
Classify quality
Readings are classified as Poor / Fair / Good / Excellent, shown on the OLED.
5
Debounce check
An issue must repeat for 3 consecutive cycles — filters out one-off noise spikes.
6
Alert via SMS
GSM module texts the user; a cooldown timer stops repeat spam alerts.
AquaTracker
8

## Slide 9
Sensor Accuracy: Calibration Formulas Used
Each reading is derived from a proper calibration model, not a raw sensor guess
Reading | Formula / Method | Why it matters
pH | 2-point buffer calibration: pH = slope × (V − V₇) + 7.0 | Matches the probe to real pH 4/7 buffer solutions for lab-accurate readings
Temperature | Steinhart-Hart thermistor equation (NTC physics model) | Converts resistance to temperature with real thermal physics, not a guess
Turbidity | Voltage → NTU polynomial: NTU = aV² + bV + c | Matches the sensor's true non-linear response curve
Water level | Median-of-5 filter + temperature- compensated speed of sound | Removes echo noise and adjusts for how temperature affects sound speed
Quality bands | Contiguous Poor / Fair / Good / Excellent thresholds | Every reading maps cleanly to one clear quality category
AquaTracker
9

## Slide 10
Reliability & Alert Features
Built into the firmware to keep readings accurate and alerts trustworthy
Non-blocking operation
Sensor readings and GSM call handling run on independent timers, so an incoming call is never missed.
Debounced alerts
An issue must show up for 3 consecutive readings before triggering an SMS — filters out one-off sensor noise.
SMS cooldown timer
A 15-minute cooldown between alerts prevents the system from repeatedly spamming the same warning.
Battery/solar monitoring
A voltage-divider reading on the 12V line means low charge is itself an SMS-worthy alert.
Median filtering
Every analog and ultrasonic reading is median-filtered to reject single-sample spikes before it's used.
Clear quality classification
Readings map to well-defined Poor / Fair / Good / Excellent bands with no ambiguous overlap.
AquaTracker
10

## Slide 11
Results & Future Scope
What the system delivers today, and where it can go next
Advantages Achieved
Calibrated, real-world-accurate pH, temperature and turbidity readings
Fewer false SMS alerts thanks to debouncing and cooldown timing
Fully solar powered — deployable anywhere with GSM signal
Low-cost, replicable hardware built entirely on Arduino UNO
Future Scope
EEPROM-stored calibration so pH/turbidity constants persist across power cycles
Cloud dashboard (via GSM GPRS/NB-IoT) alongside SMS for historical trends
Auto motor/valve control to shut off inflow once tank reaches capacity
Multi-tank support with a single GSM hub for larger sites
AquaTracker
11

## Slide 12
Thank You
AquaTracker — Smart, solar-powered, self-alerting water monitoring
Questions welcome